## Slide 1: Smart Waste Bin Project
Team 10
Vasileios Banakos - up1100950
Charalampos Papadopoulos - up1104662
Ioanna Trochatou - up1101103

## Slide 2: Problem Statement
The Problem
  Inefficient waste management in university and public buildings leads to overflowing bins and unnecessary cleaning routes.
Our Proposal
  A 'Smart Waste Bin' system that is monitored in real-time.
The Solution
  Using Passive Infrared (PIR) motion sensors to record bin usage and transmitting this data via IoT protocols to a central monitoring Dashboard.

## Slide 3: Project Objectives
Edge Intelligence: Filtering sensor 'noise' locally at the bin (debouncing) to prevent transmitting redundant data.
Data Resilience: Simultaneous local storage (JSONL) and remote transmission (MQTT) to ensure zero data loss.
Modularity: Separation of concerns by implementing the Publisher-Subscriber pattern.
Semantic Interoperability: System modeling (creating a Digital Twin) using Web Ontologies (JSON-LD).

## Slide 4: System Architecture: Hardware & Edge
Hardware: Raspberry Pi 4/5 connected to an HC-SR501 (PIR) motion sensor.
The Pipeline (Milestone 3):
  Sampler: Reads raw, high-frequency data from the GPIO pin.
  Interpreter: Applies a 5-second cooldown logic to distinguish actual waste disposal events from prolonged movement.
Local Logging: Automatic recording of every event (Timestamp, Sequence ID, CPU Temp) to an offline .jsonl file on the Edge Node.

## Slide 5: System Architecture: Network & GUI
Middleware (MQTT): Powered by a Mosquitto Broker. The Raspberry Pi acts purely as the Producer, and the Laptop as the Consumer.
The Dashboard: A custom Graphical User Interface (GUI) built with Tkinter.
Live Analytics:
  Real-time Matplotlib charts (Inter-event delays, Hourly Usage Heatmap).
  Automated visual alerts if the disposal threshold is exceeded (e.g., >10 events/hour).

## Slide 6: System Architecture: Semantic Data
Digital Twin: Implementation of Milestone 5 using JSON-LD for Semantic Web integration.
Ontologies Utilized:
  SOSA / SSN: To describe the PIR sensor capabilities and its specific observations.
  Schema.org: For defining physical bin characteristics (capacity, material, dimensions).
  BOT (Building Topology): To accurately map the bin's physical deployment location (KYPES Lab -> HMTY Building).

## Slide 7: Conclusion
Successfully established a fully functional IoT network (Sensor -> Edge Node -> MQTT Broker -> GUI Dashboard).
Demonstrated the value of Edge Computing by significantly reducing network payload through a custom Python filtering pipeline.
Modeled the physical system with Semantic Web standards, ensuring the architecture is ready for broader Smart City integrations.

## Slide 8: Possible Extensions
Containerization (Milestone 4): Wrapping the entire ecosystem (Broker, Publisher, Dashboard) into Docker Containers using docker-compose for streamlined deployment.
Additional Sensors: Integrating an Ultrasonic Sensor (e.g., HC-SR04) to directly measure the physical fill level (%) alongside motion events.
Cloud Integration & ML: Connecting the telemetry stream to a time-series database (e.g., InfluxDB) for historical analysis and predictive maintenance using Machine Learning.